## Slide 1
Table Tennis Playing Robots?!
Mohit Vikas Javale, Atharva Sunder Ramdas
Motivation
Table tennis is a fast-paced, high-dexterity task that is easy to learn but difficult to master—even for humans. A major challenge arises from the ball's lightweight and smooth design, which makes it highly susceptible to aerodynamic forces. These effects, primarily accentuated by heavy spin, significantly influence the ball’s motion and make accurate placement of the ball difficult.
Also, both of us are table tennis player and enjoy it very much: we think it would be cool to figure out what the optimal stroke looks like in many cases to improve our own gameplay : )
Goals
To figure out dynamics of interactions taking place in a table-tennis scenario and implement then to create a custom simulator.
Devise an optimal control strategy for a robotic 6DOF manipulator to successfully return a ball.
Get 2 such manipulator robots to successfully hold long rallies with one another.
Hopefully, also get this setup to where it could be deployed in real-time over actual hardware
Approach:
Focused Player: In this approach, given some initial condition of the ball, the control algorithm tries to find a solution that return the ball to a specified desired location at a specified desired time while satisfying table tennis rules.
Defensive Player: In this approach, given some initial condition, the control algorithm itself figures out an optimal location and time to return the ball, such that table tennis rules are followed over the trajectory.
Objective Function Components
Step length regularization (to prevent large step lengths)
Racket state regularization (to restrict angles to reduce striking velocity)
Reach goal state at final timestep
Problem Statement
Preliminary Results
Dynamics Equations
Ball Flight Dynamics
Accounts for gravity, air drag due to ball velocity and Magnus effect due to spin.
Implementation Details
Free-time Formulation
The problem is modelled as a free-time problem, to give the algorithm freedom to choose a striking time that makes it possible for the ball to successfully reach the goal position.
For hybrid transitions, we enforce first bounce at step, racket contact at step, and second bounce at step.
Kinematic Formulation
Trajectory optimization is done over kinematics and not dynamics due to compute limitations. (6DOF manipulator dynamics are highly non-linear)
16-745: Optimal Control and Reinforcement Learning
Future Work
Table Contact Reset Map
Accounts the interchange between linear and angular velocity due to friction and restitution.
Racket Contact Reset Map
Very similar to table contact reset map, just expressed in the racket frame.
Initial conditions
Ball Flight Dynamics
Racket Contact Reset Map
Table Contact Reset Map
Goal Position
End Effector Initial Conditions
End Effector Ball Contact Condition
UR5 Replica
Racket position, rotation, velocity
Ball Trajectory Optimization
Manipulator Trajectory Optimization
States
Constraints
Initial condition constraint
Ball flight dynamics for aerial phases
Table contact reset map at and timesteps.
Racket contact reset map at timestep.
Sum of step lengths between and equals desired return time
Step length positivity (and upper bound for safety)
Reset Map
RK4
State in Guard set
Objective Function Components
Acceleration regularization (to enforce smooth trajectories)
Reach racket state at strike time
Reach zero config state at final timestep
States
Constraints
Initial condition constraints
Kinematic derivative constraints
Make manipulator capable to hit backhand shots.
Implement defensive player formulation
Add second manipulator
Perform live optimization for both manipulators
Optimize solver for near real-time deployment
Aerial swing due to sidespin, (caused by aerodynamic effects)
Ball returning due to backspin (caused by frictional effects)
Slice shot to counter incoming backspin
Closed racket angle to counter incoming topspin